## Slide 1: The History of Nuclear Reactors

## Slide 2: Uranium Fission

## Slide 3: Uranium Fission

## Slide 4: Discovery of Nuclear fission in Germany - 1938
Otto Hahn, Fritz Strassmann, Lise Meitner, Otto Frisch
Kaiser Wilhelm Institute for Chemistry
Hahn won Nobel Prize in Chemistry 1944
Contradicted work by Fermi who believed that they were only making elements 93 and 94

## Slide 5: Pre-World War II
1939 – Francis Perrin introduced three concepts critical to nuclear reactors:
Moderation (graphite, water, or heavy water)
Critical mass
Absorbing control rods (boron, cadmium)

## Slide 6: First critical reactor: Fermi’s Pile
December 2, 1942 – Fermi reported having produced the first self-sustaining chain reaction
  Beneath the West Stands of Stagg Field (a squash-rackets court) in Chicago

## Slide 7: “A crude pile of black bricks and wooden timbers” - Fermi
No cooling system
No radiation shield or containment!
Mixture of natural uranium and graphite bricks
  771,000 lbs graphite
  81,000 lbs UO
  12,000 lbs U metal
½ Watts

## Slide 8: SCRAM!
Safety
Control
Rod
Axe
Man
-
Or is it?

## Slide 9: The first Pu production reactors for Manhattan project
Early natural uranium-fueled, water-cooled reactors constructed at Hanford, WA.
As a backup project, the X-10 Pu production reactor of air-cooled design was built at Oak Ridge, Tennessee.

## Slide 10: The Trinity Test
July 16, 1945 (5:29:45 AM) – the first nuclear explosive device was tested successfully at Alamogordo, New Mexico
It used plutonium made in a nuclear reactor
The teams did not consider it necessary to test a simpler device using 235U.

## Slide 11: Implosion Device
Well timed explosions increases the density of the Pu core, bringing the atoms closer together to achieve a critical geometry
Fat Man, Trinity

## Slide 12: Gun Type
Two subcritical masses of 235U are collided rapidly to form a dense, critical mass
2% uranium fission
Little Boy

## Slide 13: Nazi nuclear pile!
Notes: -Physicists decided not to mention to Fuhrer out of fear of what would happen if they failed
-Workers fled to US
-US much more coordinated and funded

## Slide 14: Post-World War II Era
Shortly after the end of World War II, the first enriched-fuel research reactor (14.6 w/o 235U) was completed at Los Alamos as enriched 235U became available for research purposes
At about this time, the Canadian project succeeded in building a zero-power, natural uranium-fueled research reactor, the so-called ZEEP (Zero-Energy Experimental Pile) – Heavy water
Following this, reactor production increased at a staggering pace

## Slide 15: Heavy Water Reactors
2H isotope – Deuterium
  Hydrogen with a neutron in the nucleus
D2O
  Water with two deuterium atoms
  HDO – Semi heavy water
Not as good at moderating neutrons, but absorbs significantly fewer
Neutron Capture cross section

## Slide 16: Early Nuclear Reactors
Name | Location | Operation | Fuel | Moderator
CP-1 | Chicago, IL | Dec 1942 | 50 tons natural U | graphite
X-10 | Oak Ridge, TN | Nov 1943 | natural U cylinders | graphite
CP-3 | Argonne, IL | May 1944 | natural U rods | D2O
Hanford | Hanford, WA | Sept 1944 | natural U slugs | graphite
LOPO | Los Alamos, NM | Sept 1945 | enriched 235U, UO2SO4 dissolved in H2O | H2O
ZEEP | Chalk River, Canada | Sept 1945 | natural U | D2O
Clementine | Los Alamos, NM | Nov 1946 | 239Pu rods | none
GLEEP | Harwell, England | Aug 1947 | natural U bars | graphite
NRX | Chalk River, Canada | Aug 1947 | natural U cylindrical rods | D2O
BSR | Oak Ridge, TN | Nov 1950 | enriched sandwich plates | H2O
JEEP | Kjeller, Norway | Aug 1951 | natural U rods | D2O
EBR-I | Arco, Idaho | Dec 1951 | 90% enriched U rods | none
MTR | Arco, Idaho | Mar 1952 | enriched 235U sandwich plate | H2O
APS-I | USSR | 1954 | 5% enriched U rods | graphite
PWR | USS Nautilus | Jan 1955 | highly enriched 235U | H2O
Calder Hall | Cumberland, England | Oct 1956 | natural U rods | graphite
EBWR | Argonne, IL | Dec 1956 | 1.5% 235U plates | H2O
PWR | Shippingport, PA | Dec 1957 | highly-enriched 235U and natural U | H2O
Dresden I | Morris, IL | Oct 1959 | enriched 235U | H2O

## Slide 17: Post-World War II Era (continued)
The earliest U.S. nuclear power project had been started in 1946 at Oak Ridge
  the program was abandoned in 1948 to concentrate on the naval reactor program that produced the first nuclear-powered submarine (the Nautilus)
1953 – President Dwight D. Eisenhower of the United States announced the Atoms for Peace program
  this program established the groundwork for a formal U.S. nuclear power program and expedited international cooperation on nuclear power

## Slide 18: The Nautilus

## Slide 19: 1955: The Nautilus
Reactor designed by Westinghouse
Liquid-metal cooled PWR.
Revolutionized naval warfare.
First sub to have unlimited air conditioning, range, and submerged time!
First submarine to travel underneath the ice to North Pole

## Slide 20: Victory of the PWR and BWR
During the late 1950’s and early 1960’s, a number of true commercial prototype nuclear power plants were built
Of these, the most successful were the light-water reactor and pressurized-water reactor systems
Some alternatives:
  Fast breeder reactors (perpetual energy machines!?)
  Heavy water moderated reactors (Canada CANDU)
  High-temperature gas-cooled (HTGR)
  Graphite moderated (Soviet style RBMK, Chernobyl!)

## Slide 21: Pressurized Water Reactor

## Slide 22: Boiling Water Reactor

## Slide 23: 1979: Three Mile Island

## Slide 24: A multiple fault event: who wins: machines or humans?
The feed pump in the turbine loop malfunctioned (Machine Fault 1)
This caused the reactor to SCRAM
Decay heat caused an increase in pressure
A relief valve opened to decrease the pressure
However, the valve failed to close (Machine Fault 2)
The operators incorrectly read the indicator light and thought the valve was properly closed (Human Fault 1)
42 hours prior, workers tested the emergency pump and incorrectly left a valve open causing the emergency pump to not work (Human fault 2)

## Slide 25: Multiple faults continued
During the emergency pump maintenance 42 hours prior, it was also NRC regulations to shut down the reactor (not done) so something like this couldn’t happen (Human Fault 3)
So, now the reactor was losing water and pressure due to the faulty valve and getting hotter due to the faulty emergency pump, and the operators thought the reactor was actually GAINING pressure
There was another indicator light which correctly depicted the situation, but it was behind a desk where no one could see it (Human fault 4)
Final tally: Humans: 4 Machines: 2

## Slide 26: Aftermath
During the several hours where the operators failed to grasp the situation, 60% of the fuel melted.
Some of this fuel diffused into the coolant water
The pressure relief valve released coolant water out of the containment building to an auxiliary building
Ultimately, about 17 million Curies of gaseous fission products (Xe, I, Kr) was released into the atmosphere
No statistically significant increase in cancer in surrounding area

## Slide 27: 1986 Chernobyl: super-prompt critical incident

## Slide 28: Greedy Soviet design flaws!
1) Graphite moderator w/ water coolant, 2) positive coolant void coefficient, 3) control rods tipped with graphite, 4) no containment building

## Slide 29: What went wrong?
A special safety test of the turbine was supposed to take place around 1 pm when electricity demand was low (test called for lowering and increasing power)
An unusually cold Russian day caused the test to be delayed…
11:10 pm: The test and power reduction resumed
12:00 am: Shift change. Now only electrical engineers knew what was going on
The electrical engineers then attempted to raise the power levels

## Slide 30: What went wrong continued
But fission-product poisons caused the reactor to take a long time to increase power
To speed up this process, they started to withdraw control rods:
  Operating procedure: always leave at least 30 rods inserted
  They had 205 rods withdrawn and only 6 rods inserted
Suddenly power began to rise rapidly
The emergency control rods were lowered and the sudden introduction of the graphite tips caused the reactor to go super-prompt critical
Power was at 300,000 MW
Two thermal explosions

## Slide 31: Summary of Facts
April 26, 1986:
  Chernobyl nuclear power plant
    Operator errors cause a reactor explosion
    Explosion releases 190 tons of radioactive gasses into the atmosphere
    Fire starts that lasts 10 days
People:
  7 million lived in contaminated areas; 3 million were children
Wind:
  Carries radiation far distances

## Slide 32: Radioactive fallout

## Slide 33: Human Impact
5.5 million people still live in contaminated areas
31 people died in 3 months of radiation poisoning
134 emergency workers suffered from acute radiation sickness
Cancer afflicts many others: estimates of cancers attributable to Chernobyl range from ~5,000 to 20,000 (vast majority are thyroid cancers)

## Slide 34: Environmental impact: wildlife paradise?

## Slide 36: Old sarcophagus

## Slide 37: New sarcophagus

## Slide 38
Fukushima

## Slide 39
Fukushima
March 11th, 2011
Large earthquake (9.0) off coast of Japan
BWR Style Reactor

## Slide 40
Fukushima
3 backup power systems failed to run cooling system pumps
  Knocked out off site power
  Flooded emergency diesel generators
  Batteries eventually died
1,2,3 operating
4 offline and defueled
5 and 6 cold shutdown

## Slide 41
Fukushima
March 12th
Hydrogen explosion in reactor 1 destroys building, exposing spent fuel pools
Zr + 2H2O -> ZrO2 + H2 at high temperatures
March 14th
Reactor 3 hydrogen explosion
March 15th
Reactor 2 hydrogen explosion

## Slide 42
Fukushima
March 16th
Efforts to maintain spent fuel pool temperatures are main effort, seawater used
Containments still in place for reactor

## Slide 43: Fukushima Effects
No direct fatalities due to radiation
Long term cancer effects estimated to impact 130-640 people
1,600 deaths due to the poor evacuation plans
April 29th, 2011

## Slide 44: New Nuclear Power Plants

## Slide 45: Advanced Reactors
VTR
US DOE
NuScale
NuScale, LLC

## Slide 46: Nukes in Space!

## Slide 47: How Nukes Work

## Slide 48
for 1 kg of coal, assuming 100% C,

## Slide 49
https://i.pinimg.com/originals/87/dc/45/87dc450874b56fb68ce0586ca5c8e147.jpg

## Slide 52
for 1 kg of uranium, assuming 0.72% 235U,
or if we assume use in an advanced reactor:
(1 kg coal )

## Slide 54
www.nrc.gov

## Slide 55
http://www.world-nuclear.org/uploadedFiles/org/WNA/Publications/Working_Group_Reports/comparison_of_lifecycle.pdf

## Slide 56
Chart: Estimated Cost Comparison of Energy Sources Planned by 2022
| Conventional CC | Advanced CC | Advanced CT | Advanced nuclear | Geothermal | Biomass | Wind, onshore | Wind, offshore | Solar PV | Hydroelectric
Capital | 13 | 15.5 | 22.7 | 67 | 28.3 | 40.3 | 33 | 102.6 | 48.2 | 56.7
O&M | 1.5 | 1.3 | 2.6 | 12.9 | 13.5 | 15.4 | 12.7 | 20 | 7.5 | 14
Fuel | 32.8 | 30.3 | 51.3 | 9.3 | 0 | 45 | 0 | 0 | 0 | 1.3
Transmission | 1 | 1.1 | 2.9 | 0.9 | 1.3 | 1.5 | 2.4 | 2 | 3.3 | 1.8
Natural Gas
Dispatchable
Non-Dispatchable
$16B*

## Slide 61
https://www.nextbigfuture.com/2012/06/deaths-by-energy-source-in-forbes.html
World supply is 150,000 TWh/y

## Slide 65
Ye shall know the truth and the truth shall set you free

## Slide 66: How Nukes Work
How is nuclear power different from chemical power sources?
How do nuclear power plants generate electricity?
Isn’t nuclear power / waste dangerous?
What about the risk of nuclear weapons?
Union of Concerned Scientists: https://www.ucsusa.org/nuclear-power/cost-nuclear-power/retirements?_ga=2.68367313.1717052947.1542400265-1929339798.1542306463#.W-8pJ-hKiUk
Bill Nye on Fukushima: https://www.youtube.com/watch?v=bcXf6aWt4hI
John Oliver on nuclear waste: https://www.youtube.com/watch?v=ZwY2E0hjGuU
Iran deal: https://www.youtube.com/watch?v=oqvghou5m3U
Monitoring for nuclear tests: https://www.youtube.com/watch?v=daZ7IQFqPyA